DATA SHEETS .... EPM & M660nm 5mW ....RED LASER MODULE

| Barrel Specs: 3/8 - 56 Thread Size Dia: 10.4mm Length: 17mm | Collect Specs: 3/8 - 56 Thread Size 4.3mm Aperture Half Hard Brassbbb | Lens Housing Specs: 3/8 - 56 Thread Size 3.7mm Aperture 7mm Plastic Lens |
| --- | --- | --- |

RED LASER DIODE  ABSOLUTE MAXIMUM RATINGS - (Tc=25 °C)

| TECHNICAL DATA Visible light output 660nm Optical power output 5mW CW Package Type 5.6mm Built-in photo diode for monitoring laser output | Pin Out Diagram - Style A |
| --- | --- |

| Items | Symbols | Values | Unit |
| --- | --- | --- | --- |
| Optical output power | Po | 5 | mW |
| Laser diode reverse voltage | V | 2 | V |
| Photo diode reverse voltage | V | 30 | V |
| Operating temperature | Topr | -10 ~ +60 | °C |
| Storage temperature | Tstg | -40 ~ +85 | °C |

OPTICAL and ELECTRICAL CHARACTERISTICS - (Tc=25 ºC)

| Items | Symbols | Min. | Typ. | Max. | Unit | Test Condition |
| --- | --- | --- | --- | --- | --- | --- |
| Optical output power | Po | - | 5 | - | mW | - |
| Threshold current | Ith | - | 20 | 40 | mA | - |
| Operating current | Iop | - | 40 | 60 | mA | Po=5mW |
| Operating voltage | Vop | - | 2.7 | - | V | Po=5mW |
| Lasing wavelength |  | 655 | 660 | 665 | nm | Po=5mW |
| Beam divergence |  | - | 5 | 11 | deg | Po=5mW |
| Beam divergence |  | - | 25 | 37 | deg | Po=5mW |
| Monitor current | Is | - | 10 | 20 | uA | Po=5mW |
| Astigmatism | As | - | 11 | - | um | Po=5mW |
| MTTF |  |  | 10000 hrs |  |  | Po=5mW |

| Emitter Size | 10 x 60 Microns - Emitter Distance to Cap Lens = 0.3mm |
| --- | --- |
| Structure | Index Guided |