Embedded C code

#include <Mega32.h>

#include <delay.h>

#include <stdio.h>

//#include <90s8515.h>

#define begin {

#define end }

//#define led PORTB

#define incr 80

#define cw 1

#define ccw -1

#define Vertical   0

#define Horizontal 1

#define debounce 10

#define maxkeys 16

#define tolerance 30

#define gracePeriod 5 //seconds given to leave the room

#define maxAttempts 3 //number of tries given to disarm before sounding alarm

#define vibDuration 1 //number of seconds to consider the same vibration

#define disarmTime 10 //seconds allowed to disarm system before alarm sounds

//NOTES: Connect to Hyperterminal at 115.2kHz

//PORTA connect to motor controller

//PORTB connect to LEDs

//PORTC connect to keypad

//PORTD connect to hardware (for ICP, reset) and for RX/TX

//Don't forget to tie a two cable jumper from Rx, Tx pins to PORT D (white wire is Rx Green is Tx)

signed char shortPath(unsigned char, unsigned char, unsigned char);

void motor(unsigned char, char, unsigned char, char);

//States for keypad operation

enum { disarm, armed, teach_motor, teach_code, maybe_armed, leaveRoom, intruder, violation };

unsigned char key, butnum, prevButnum;

//key pad scan table

flash unsigned char keytbl[16]={0xee, 0xde, 0xbe, 0xed, 0xdd, 0xbd, 0xeb, 0xdb, 0xbb, 0xd7, 0x7e, 0x7d, 0x7b, 0x77, 0xe7, 0xb7};

enum{pushed,notPushed,maybePushed,maybeNotPushed};

unsigned char terminate,flag;

unsigned int counter;

unsigned int t1,t2,t3,t4;

unsigned char eventCounter;

unsigned char i, steps;

signed char phaseH, phaseV, directionH, directionV;

signed char motor_h, motor_v;

signed char sensh[10],sensv[10];

unsigned char beatFlag, newKey;

unsigned int beat,keyBeat,prevKeyBeat;

unsigned char code[5], attempt_code[5];

unsigned int rhythm[5], attempt_rhythm[5];

unsigned char state,entry,prevstate;

unsigned int seconds_counter;

unsigned long seconds,vibTime;

unsigned char failure;

unsigned int countDown;

unsigned char rhythmHelper;

unsigned char mostRecentlyTriggered;

signed char dirH, dirV;

unsigned char newCode;

unsigned char changeLocation;

unsigned char sensorIndex;  //sensor to be displayed/modified

unsigned char quickView;

unsigned char disarmCntdn;

unsigned char alarm;

//Use input capture pin (ICP) to timestamp a trigger event using

//Timer1

interrupt [TIM1_CAPT] inputCapt(void)

begin

unsigned char violationIndex,tempH,tempV;

//quickView = PINB;

//led = ~ICR1L;

//D.7 --> reset for Schmidtt Trigger 4

//D.6 --> ICP pin

//D.5 --> reset for Schmidtt Trigger 3

//D.4 --> reset for Schmidtt Trigger 2

//D.3 --> INT1 -- reset for Schmidtt Trigger 1

//Sensor 1 triggered the interrupt

/*	if (!PINB.0) printf("sensor 1 triggered first\n\r");

if (!PINB.1) printf("sensor 2 triggered first\n\r");

if (!PINB.2) printf("sensor 3 triggered first\n\r");

if (!PINB.3) printf("sensor 4 triggered first\n\r");

*/

//printf("%d\n\r",quickView);

//Reset Schmidtt Triggers

//DDRD = 0xB8; //Flash on reset signal to sensor

//delay_ms(100);	//Length of time to place 5V on Schmitt for reset

//DDRD = 0x00; //return all pins to input pins

printf("in the ICP routine");

if ((DDRB & 0x0f) == 0x00) //indicates this is the first sensor to trigger

begin

printf("first sensor triggered\n\r");

TCNT1 = 0; //reset timer;

end

//Disable sensors already triggered by forcing output high

if (!PINB.0) begin

t1 = ICR1H;

t1 = t1 << 8;

t1 = t1 | ICR1L;

printf("turing off sensor1\n\r");

DDRB.0 = 1;

PORTB.0 = 1;

printf("%d\n\r",DDRB);

violationIndex = 1;

end

else if (!PINB.1) begin

t2 = ICR1H;

t2 = t2 << 8;

t2 = t2 | ICR1L;

printf("turning off sensor2\n\r");

DDRB.1 = 1;

PORTB.1 = 1;

printf("%d\n\r",DDRB);

violationIndex = 2;

end

else if (!PINB.2) begin

t3 = ICR1H;

t3 = t3 << 8;

t3 = t3 | ICR1L;

printf("turning off sensor3\n\r");

DDRB.2 = 1;

PORTB.2 = 1;

printf("%d\n\r",DDRB);

violationIndex = 3;

end

if (!PINB.3) begin

t4 = ICR1H;

t4 = t4 << 8;

t4 = t4 | ICR1L;

printf("turning off sensor4\n\r");

DDRB.3 = 1;

PORTB.3 = 1;

printf("%d\n\r",DDRB);

violationIndex = 4;

end

//outputs to VB program if state = armed and a new vibration occurs

if ((state == armed) & (seconds - vibTime)>vibDuration) begin

printf("Violation\n\r");

alarm = 1;

printf("%d\n\r", violationIndex);

//Take a picture of violation

//First, slew motors - have motor take shortest path to desired location

tempH = shortPath(sensh[violationIndex], motor_h,Horizontal);

tempV = shortPath(sensv[violationIndex], motor_v,Vertical);

motor(tempH,dirH,tempV,dirV);

//Invoke VB picture command

printf("Video Capture\n\r");

vibTime = seconds;

printf("%d\n\r",vibTime);	//Used to timestamp picture

end

//reset Schmidtt Triggers

DDRB = 0x1f;           //NOTE: LED on PORTB.4

PORTB = 0x0f;

delay_ms(100);

DDRB = 0x10;

/*if ((DDRB & 0x0f) == 0x0f) //indicates all four sensors have been triggered

begin

printf("all four sensors triggered, resetting...\n\r");

//reset the PORTB pins to inputs

PORTB = (PORTB & 0xf0);

DDRB = (DDRB & 0xf0);

printf("T1: %d , T2: %d , T3: %d , T4: %d\n\r",t1,t2,t3,t4);

//reset schmidtt Triggers

//DDRD = 0xB8; //Flash on reset signal to sensor

//delay_ms(100);	//Length of time to place 5V on Schmitt for reset

//DDRD = 0x00; //return all pins to input pins

end*/

/*if (eventCounter == 4) eventCounter = 0;

switch (eventCounter)

begin

case 0:

TCNT1 = 0; //reset counter;

printf("Timer start");

break;

case 1:

t1 = ICR1H;

t1 = t1 << 8;

t1 = t1 | ICR1L;

printf("Time1: %d\n\r",t1);

break;

case 2:

t2 = ICR1H;

t2 = t2 << 8;

t2 = t2 | ICR1L;

printf("Time2: %d\n\r",t2);

break;

case 3:

t3 = ICR1H;

t3 = t3 << 8;

t3 = t3 | ICR1L;

printf("Time3: %d\n\r",t3);

//Reset Schmidtt Trigger

DDRD = 0xB8; //Flash on reset signal to sensor

delay_ms(100);	//Length of time to place 5V on Schmitt for reset

DDRD = 0x00; //return all pins to input pins

break;

default:

eventCounter = 0;

break;

end

eventCounter++;	*/

end

interrupt [TIM0_OVF] overflow(void)

begin

//overflows every 16us

seconds_counter++;

if (seconds_counter == 62500) begin

seconds++;

seconds_counter = 0;

if (disarmCntdn <= disarmTime) //implies the countdown hasn't looped back around yet

begin

disarmCntdn--;

end

end

counter++;

if (counter == 1250) //occurs every 20ms

begin

countDown--;

beatFlag = 1;

beat++;

counter = 0;

end

end

//Alert user when violation occurs

interrupt [EXT_INT0] void ext_int0_isr(void)

begin

signed int violationIndex;

int tempH, tempV; //keeps horiz/vert motor positions

/*(non-vibration) sensors

PINB.5 ... Sensor 5

PINB.6 ... Sensor 6

PINB.7 ... Sensor 7

NOT IMPLEMENTED PIN X ... Sensor 8

*/

printf("Violation\n\r");

if (!PINB.5) violationIndex = 5;

else if (!PINB.6) violationIndex = 6;

else if (!PINB.7) violationIndex = 7;

//else if (!PINB.3) violationIndex = 4;

else begin

printf("Interrupt error!\n\r");

violationIndex = 0;

end

//if (violationIndex != mostRecentlyTriggered)

//begin

printf("%d\n\r", violationIndex);

if (violationIndex != 0)

begin

//Take a picture of violation

//First, slew motors - have motor take shortest path to desired location

tempH = shortPath(sensh[violationIndex], motor_h,Horizontal);

tempV = shortPath(sensv[violationIndex], motor_v,Vertical);

motor(tempH,dirH,tempV,dirV);

alarm = 1;

//Invoke VB picture command

printf("Video Capture\n\r");

printf("%d\n\r",seconds);	//Used to timestamp picture

end

//end

MCUCR = 0x00;      //trigger on falling edge

GICR = 0x00;

mostRecentlyTriggered = violationIndex;

end

void initialize(void)

begin

unsigned char j;

//setup PORTA for driving motor

DDRA = 0xff;

PORTA = 0x00;

//setup PORT D.6 as ICP pin (input) enable pullups

//D.7 --> reset for Schmidtt Trigger 4          Not Necessary

//D.6 --> ICP pin

//D.5 --> reset for Schmidtt Trigger 3          Not Necessary

//D.4 --> reset for Schmidtt Trigger 2          Not Necessary

//D.3 --> INT1 -- reset for Schmidtt Trigger 1  Not Necessary

//D.2 --> INT0

//D.1 --> TXD

//D.0 --> RXD

//flash pattern 0xB8 for reset

DDRD = 0x00;

PORTD = 0xff;

//implement sensor reset button using button SW0

//setup buttons as portC

DDRC = 0x00;

PORTC = 0xff;

//implement PORTB as input from sensors and as led blinker on PORTB.4

DDRB = 0x10;

//setup Timer1 for input capture function

TCCR1A = 0x00;

TCCR1B = 0b10000011; //ICP Enable Noise Canceler, Falling edge, Normal Mode, Clk/64

//setup Timer0 for beat management

TCCR0 = 0x00000001; //Clk/1 prescaler

TIMSK = 0b00100001;	//Input Capture Interrupt Enable, Enable interrupt on overflow Timer0

mostRecentlyTriggered = 0;

//setup button state machine

terminate = 0;

counter = 0;

phaseV = 0;

phaseH = 0;

directionH = 0;

directionV = 0;

motor(2,0,2,0);

flag = 0;

//state = notPushed;

eventCounter = 0;

motor_h = 0; //horizontal position

motor_v = 0; //vertical position

changeLocation = 0;

//Initialize keypad variables

//UCR = 0x10 + 0x08 ;

//UBRR = 25 ;

//States for keypad operation

state = disarm;

printf("Disarmed: Ready\n\r");

//Time

seconds_counter = 0;

vibTime = 0;

seconds = 0;

prevKeyBeat = 0;

entry= 5;

failure = 0;

alarm = 0;

sensorIndex = 1;

newCode = 0;

rhythmHelper = 100;

//Default code

code[0] = 0; code[1] = 0; code[2] = 0; code[3] = 0; code[4] = 0;

rhythm[0] = 0; rhythm[1] = 80; rhythm[2] = 127; rhythm[3] = 176; rhythm[4] = 226;

for (j = 0; j<5; j++) begin

attempt_code[j] = 0;

attempt_rhythm[j] = 0;

end

//Reset Schmidtt Trigger

DDRB = 0x1f;           //NOTE: LED on PORTB.4

PORTB = 0x0f;

delay_ms(100);

DDRB = 0x10;

//DDRD = 0xB8; //Flash on reset signal to sensor

//delay_ms(100);	//Length of time to place 5V on Schmitt for reset

//DDRD = 0x00; //return all pins to input pins

//Disable unused vibration sensors

//DDRB = (DDRB & 0xf0)|0x0c;

//PORTB = DDRB;

//turn on LED

PORTB.4 = 0;

#asm("sei");

end

void disp_time()

begin

printf("Time:\n\r");

printf("%d seconds\n\r", seconds);

end

void get_cmd_init()

begin

UCSRB = 0b10011000;

UBRRL = 8; //115.2k baud //103;  //9600 Baud

end

void motor(unsigned char stepsH, char directionH, unsigned char stepsV, char directionV)

begin

//routine for stepper motor

//PORTA: 7   6   5   4   3   2  1  0

//      CE1 IN1 CE2 IN2

unsigned char mask;

for (i=0; i<stepsH; i++)

begin

//

motor_h = motor_h + directionH;

if (motor_h >= 48) motor_h = 0;

else if (motor_h < 0) motor_h = 47;

//led = ~ motor_h;

phaseH = phaseH + directionH;

if (phaseH > 4) phaseH = 1;

if (phaseH <= 0) phaseH = 4;

mask = PORTA & 0b00001111;

switch (phaseH)

begin

//        A B A B

case 1:

//step 1: + + - -

PORTA = 0b10100000 | mask;

delay_ms(incr);

break;

case 2:

//step 2: - + + -

PORTA = 0b11100000 | mask;

delay_ms(incr);

break;

case 3:

//step 3: - - + +

PORTA = 0b11110000 | mask;

delay_ms(incr);

break;

case 4:

//step 4: + - - +

PORTA = 0b10110000 | mask;

delay_ms(incr);

break;

case 5:

//step 5: + + - -

PORTA = 0b10100000 | mask;

delay_ms(incr);

break;

end

end

//routine for stepper motor

//PORTA: 7   6   5   4   3   2  1  0

//                     CE1 IN1 CE2 IN2

mask = 0b11110000 & PORTA;

for (i=0; i<stepsV; i++)

begin

//

motor_v = motor_v + directionV;

if (motor_v >= 48) motor_v = 0;

else if (motor_v < 0) motor_v = 47;

//led = ~ motor_v;

phaseV = phaseV + directionV;

if (phaseV > 4) phaseV = 1;

if (phaseV <= 0) phaseV = 4;

switch (phaseV)

begin

//        A B A B

case 1:

//step 1: + + - -

PORTA = 0b00001010 | mask;

delay_ms(incr);

break;

case 2:

//step 2: - + + -

PORTA = 0b00001110 | mask;

delay_ms(incr);

break;

case 3:

//step 3: - - + +

PORTA = 0b00001111 | mask;

delay_ms(incr);

break;

case 4:

//step 4: + - - +

PORTA = 0b00001011 | mask;

delay_ms(incr);

break;

case 5:

//step 5: + + - -

PORTA = 0b00001010 | mask;

delay_ms(incr);

break;

end

end

//PORTA = 0x00;

end

signed char shortPath(unsigned char sens, unsigned char motor, unsigned char HV)

begin

signed char temp;

temp = sens - motor;

if (temp > 24) temp = temp - 48;

else if (temp < -24) temp = temp + 48;

if (temp < 0) begin

if (HV == Horizontal) dirH = ccw;

else dirV = ccw;

temp=-temp;

end

else

begin

if (HV == Horizontal) dirH = cw;

else dirV = cw;

end

return temp;

end

void main(void)

begin

signed char temph, tempv, temp,j;

unsigned char digit, opnum;

unsigned char oldCode;

get_cmd_init();

initialize();

while(1)

begin

if (beatFlag)

begin

beatFlag = 0;

//Keypad

//	while(KeyFlagA){

//get lower nibble

DDRC = 0x0f;

PORTC = 0xf0;

delay_us(5);

key = PINC;

//get upper nibble

DDRC = 0xf0;

PORTC = 0x0f;

delay_us(5);

key = key | PINC;

//find matching keycode in keytbl

if (key != 0xff)

{

for (butnum=0; butnum<maxkeys; butnum++)

{

if (keytbl[butnum]==key)  break;

}

if (butnum==maxkeys) butnum=0;

else butnum++;	   //adjust by one to make range 1-16

}

else butnum=0;

opnum = 0;

//debounce keypad

if (prevButnum == 0 && butnum != 0) newKey = 1;

if(newKey == 1)

begin

newKey = 0;

//process newKey by assigning incrementing beat count

keyBeat = beat; //update beat number

if ((keyBeat - prevKeyBeat) < debounce)

begin

//button press did not really occur... erase its existence

keyBeat = prevKeyBeat;

end

else begin

prevKeyBeat = keyBeat;

opnum = butnum;

end

end

prevButnum = butnum;

//printf("button Pressed = %d beat = %d\r",butnum,keyBeat);

//          printf("beat = %d\r",keyBeat);

//butnum code:

// 0 => no button pressed

// 1-9 => 1-9

// 10 => 0 ; 11 => A ; 12 => B ; 13 => C ; 14 => D ; 15 => * ; 16 => #

switch(state) begin

case(disarm):

if(state != prevstate) printf("Disarmed: Ready\n\r");

//disp_time();

prevstate = state;

//Disalbe external interrupt 0

MCUCR = 0x00;      //trigger on falling edge

GICR = 0x00;        //set the INT0 bit to enable external interrupt 0

if (opnum == 11) /* pressed 'A' */ 	state = teach_code;

else if (opnum == 12) /*pressed 'B' */ state = teach_motor;

else if (opnum == 15) /*pressed '*' */ state = maybe_armed;

break;

case(teach_code):

if (state != prevstate) printf("Teach new code\n\r");

prevstate = state;

//blink LED at 1Hz for synchronizing rhythm, background blink at .25Hz

if (beat%rhythmHelper == 1)

begin

PORTB.4 = ~PORTB.4;

end

//if (beat%25 == 1) PORTB.4 = ~PORTB.4;

if(opnum == 11) 	/*button 'A' pressed*/ 	begin

state = teach_motor;

PORTB.4 = 0;

end

else if(opnum == 12) /*button 'B' pressed*/ begin

state = disarm;

PORTB.4 = 0;

end

else if (opnum == 16) //enter button pressed

begin

printf("Enter old code\n\r");

oldCode = 1;

end

//CODE TEACHING MODE button D

else if (opnum == 14) //D button hit... begin teaching new code

begin

rhythmHelper = 25;

beat = 0; //restart beat number

entry = 1;

if (oldCode == 1)

begin

for (j = 1; j < 5; j++)

begin

attempt_code[j] = 0;

attempt_rhythm[j] = 0;

end

end

else

begin

//for (j = 1; j < 5; j++)

//begin

//	code[j] = 0;

//	rhythm[j] = 0;

//end

end

end

else if (opnum != 0 && opnum <= 10) //number between 0 and 9 is pressed

begin

if (entry < 5)

begin

if (opnum == 10) digit = 0;

else digit = opnum;

if (oldCode == 1)

begin

attempt_code[entry] = digit;

attempt_rhythm[entry] = keyBeat;

end

else if(newCode == 1)

begin

code[entry] = digit;

rhythm[entry] = keyBeat;

end

entry++;  //increment code entry

if ((entry == 5) && (oldCode == 1))

begin

for (j = 1; j<5; j++)

begin

if (!((attempt_code[j] == code[j]) &&

(attempt_rhythm[j] < rhythm[j]+tolerance) &&

(attempt_rhythm[j] > rhythm[j]-tolerance)))

begin

rhythmHelper = 100;

failure++;

printf("invalid attempt\n\r");

//Uncomment for debugging purposes!

/*printf("invalid disarm sequence, try again\n\r");

printf("attemped code   attempted rhythm    acutal code      actual rhythm\n\r");

printf("%d                %d               %d                 %d\n\r",attempt_code[1],attempt_rhythm[1],code[1], rhythm[1]);

printf("%d                %d               %d                 %d\n\r",attempt_code[2],attempt_rhythm[2],code[2], rhythm[2]);

printf("%d                %d               %d                 %d\n\r",attempt_code[3],attempt_rhythm[3],code[3], rhythm[3]);

printf("%d                %d               %d                 %d\n\r",attempt_code[4],attempt_rhythm[4],code[4], rhythm[4]);

*/

break;

end

end

if (j == 5)

begin

printf("Code Validated\n\r");

oldCode = 0;

newCode = 1;

rhythmHelper = 100;

//printf("Press 'D' and enter new code.\n\r");

end

end

else if ((entry == 5) && oldCode == 0)

begin

printf("New Code Entered:\n\r");

printf("%d %d %d %d\n\r",code[1],code[2],code[3],code[4]);

printf("%d %d %d %d\n\r",rhythm[1],rhythm[2],rhythm[3],rhythm[4]);

newCode = 0;

rhythmHelper = 100;

end

end

end

break;

case(maybe_armed):

if (state != prevstate) printf("maybe armed\n\r");

prevstate = state;

if(opnum == 5) //User trying to arm system

begin

if (PINB == 0xef)

begin

countDown = gracePeriod*50; 	//convert gracePeriod into seconds

state = leaveRoom;

failure = 0;

end

else begin

printf("Zone Fault: %d",PINB);

state = disarm;

end

end

else if(opnum == 11) //alert Police

begin

printf("Panic: Police\n\r");

state = disarm;

end

else if(opnum == 12) //alert Fire

begin

printf("Panic: Fire\n\r");

state = disarm;

end

else if(opnum == 13) //alert Ambulance

begin

printf("Panic: Ambulance\n\r");

state = disarm;

end

else if(opnum == 1) //special test to reset Schmidtt Triggers

begin

//Reset Schmidtt Trigger

DDRB = 0x1f;           //NOTE: LED on PORTB.4

PORTB = 0x0f;

delay_ms(100);

DDRB = 0x10;

state = disarm;

//DDRD = 0xB8; //Flash on reset signal to sensor

//delay_ms(100);	//Length of time to place 5V on Schmitt for reset

//DDRD = 0x00; //return all pins to input pins

end

break;

case (leaveRoom):

if (countDown == 0)

begin

state = armed;

rhythmHelper = 100;

end

break;

case (armed):

if (state!= prevstate) printf("armed\n\r");

prevstate = state;

//if (beat%25 == 1) led = ~led;

//Enable external interrupt 0

MCUCR = 0x02;

GICR = 0x40;        //set the INT0 bit to enable external interrupt 0

//blink LED at 1Hz for synchronizing rhythm, background blink at .25Hz

if (beat%rhythmHelper == 1)

begin

PORTB.4 = ~PORTB.4;

end

//rhythmHelper = 25; //return rhythmHelper to 1Hz

//if (beat%25 == 1) PORTB.4 = ~PORTB.4;

//sound alarm if too many bad attempts or user times out

if ((failure == maxAttempts) || (disarmCntdn == 0))

begin

printf("Keypad violation\n\r");

printf("Alarm is Sounding!\n\r");

failure = 0;

printf("9\n\r");

//Take a picture of keypad

//First, slew motors - have motor take shortest path to desired location

//Sensor 9 will be the keypad location

temph = shortPath(sensh[9], motor_h,Horizontal);

tempv = shortPath(sensv[9], motor_v,Vertical);

motor(temph,dirH,tempv,dirV);

//Invoke VB picture command

alarm = 1;

printf("Video Capture\n\r");

printf("%d\n\r",seconds);	//Used to timestamp picture

end

if (opnum == 14) //D button hit... begin disarm attempt

begin

printf("begin disarm attempt\n\r");

beat = 0; //restart beat number

rhythmHelper = 25;	//begin LED on fresh blink sequence

PORTB.4 = 1;	//turn off led

if (failure == 0) //begin Disarm Period

begin

disarmCntdn = disarmTime;

end

entry = 1;

for (j = 1; j < 5; j++)

begin

attempt_code[j] = 0;

attempt_rhythm[j] = 0;

end

end

else if (opnum != 0 && opnum <= 10) //number between 0 and 9 is pressed

begin

if (entry < 5)

begin

if (opnum == 10) digit = 0;

else digit = opnum;

attempt_code[entry] = digit;

attempt_rhythm[entry] = keyBeat;

entry++;  //increment code entry

if (entry == 5)

begin

for (j = 1; j<5; j++)

begin

if (!((attempt_code[j] == code[j]) &&

(attempt_rhythm[j] < rhythm[j]+tolerance) &&

(attempt_rhythm[j] > rhythm[j]-tolerance)))

begin

failure++;

rhythmHelper = 100;

printf("%d %d %d %d",attempt_code[1],attempt_code[2],attempt_code[3],attempt_code[4]);

printf("invalid disarm sequence, failure: %d\n\r",failure);

break;

end

end

if (j == 5)

begin

printf("Alarm disarmed\n\r");

alarm = 0;

PORTB.4 = 0;

state = disarm;

end

end

end

end

break;

//case(violation):

//Detect if sensor has been tripped

//break;

case(teach_motor):

if(state != prevstate) printf("Teach motor\n\r");

prevstate = state;

if(opnum == 11) /*button 'A' pressed*/

begin

state = disarm;

changeLocation = 0;

end

else if(opnum == 12) /*button 'B' pressed*/

begin

state = teach_code;

changeLocation = 0;

end

//Selecting sensor

//Increment is "C" (opnum 13)

if (opnum == 13) begin

sensorIndex++;

changeLocation = 0;

if (sensorIndex >= 10) sensorIndex = 1;

printf("Current location of sensor:\n\r %d \n\r %d \n\r %d\n\r", sensorIndex, sensh[sensorIndex], sensv[sensorIndex]);

printf("Press enter to edit sensor location\n\r");

end

//Decrement is "D" (opnum 14)

else if	(opnum == 14) begin

sensorIndex--;

changeLocation = 0;

if (sensorIndex <= 0) sensorIndex = 9;

printf("Current location of sensor:\n\r %d \n\r %d \n\r %d\n\r", sensorIndex, sensh[sensorIndex], sensv[sensorIndex]);

printf("Press enter to edit sensor location\n\r");

end

//Enter button pressed #

else if (opnum == 16 && !changeLocation) begin

temph = shortPath(sensh[sensorIndex],motor_h,Horizontal);

tempv = shortPath(sensv[sensorIndex],motor_v,Vertical);

motor(temph,dirH,tempv,dirV);

changeLocation = 1;

printf("Slew Motor using 2,6,8,4\n\r");

end

//MOTOR CONTROL

//Horizontal control

else if(opnum == 2) motor(1,ccw, 0, 0);

else if(opnum == 8)  motor(1,cw, 0, 0);

//Vertical control

else if(opnum == 4) motor(0,0,1,ccw);

else if(opnum == 6) motor(0,0,1,cw);

//MOTOR TEACH button #

else if(opnum == 16 && changeLocation == 1)

begin

changeLocation = 0;

sensh[sensorIndex] = motor_h;

sensv[sensorIndex] = motor_v;

printf("Current location of sensor:\n\r %d \n\r %d \n\r %d\n\r", sensorIndex, sensh[sensorIndex], sensv[sensorIndex]);

printf("New sensor position saved\n\r");

end

//MOTOR RECALL button *

else if(opnum == 15) begin

//led = ~sensh[1];

//have motor take shortest path to desired location

temph = shortPath(sensh[sensorIndex], motor_h,Horizontal);

tempv = shortPath(sensv[sensorIndex], motor_v,Vertical);

//slew motor to sensor location

motor(temph,dirH,tempv,dirV);

end

break;

end

//led = ~ opnum;

//led = 0x55;

/*DDRD = 0x80; //Flash on reset signal to sensor

delay_ms(100);	//Length of time to place 5V on Schmitt for reset

DDRD = 0x00; //return all pins to input pins

terminate = 0;

*/

end

end

end

/*while(!terminate)

begin

if (flag)

begin

flag = 0;

switch(state)

begin

case notPushed:

//led = ~0x01;

if (PINC == 0xfe)

begin

state = maybePushed;

end

break;

case maybePushed:

//led = ~0x02;

if (PINC == 0xfe) state = pushed;

else state = notPushed;

break;

case pushed:

//led = ~0x04;

if (PINC != 0xfe) state = maybeNotPushed;

break;

case maybeNotPushed:

//led = ~0x08;

if (PINC == 0xfe) state = pushed;

else

begin

state = notPushed;

terminate = 1;

end

break;

end

end

end*/

//Runs once every button SW0 press