Appendix

Specific Areas worked on by group members:

Justin Constant:

- 50% of PC Board Soldering and Whiteboard wiring

- 35% of Coding

  - Add, Delete, Debug admin functions

  - Sensor Calibrations

- Tubing System

- 50% of Report

Derek Bentson:

- 50% of PC Board Soldering and Whiteboard wiring

- 65% of Coding

  - Code Verification

  - Key Debouncing

  - State System

  - ADC reading

- 50% of Report

Datasheets for Parts Used:

Gas Sensor:  http://www.figaro.co.jp/en/pdf/2620ProductInfo0105.pdf

Pressure Sensor:  http://www.freescale.com/files/sensors/doc/data_sheet/MPX2050.pdf

STK500:  http://elmicro.com/files/stk500userguide.pdf

Atmel Mega32:  http://instruct1.cit.cornell.edu/courses/ee476/AtmelStuff/full32.pdf

Code:

/*

ECE476 Final Project Code - Breathalyzer Door Lock

Derek Bentson and Justin Constant

05/05/05

PORT A.0, A.1 used for pressure and vapor sensors

PORT B used for the keypad

PORT C used for the LCD

PORT D used for solenoid output

*/

#include <Mega32.h>

#include <delay.h>

#include <stdio.h>

#include <stdlib.h>

#include <math.h>

#asm

.equ __lcd_port=0x15

#endasm

#include <lcd.h> // LCD driver routines

#define LCDwidth 16 //characters

#define t1 	2000 		// two second delay

#define t2	10000          // ten second delay

#define t3 	30              // 30 ms delay

#define MAXKEYS 12

#define begin {

#define end   }

#define MAXCODES 12

#define CODELENGTH 4

#define AREF 			5.f	//Analog Reference Voltage

#define PRESSURE_THRESH          38	//threshold for if balloon has filled in scaled value (0-255)

#define VAPOR_THRESH    	68      //threshold for gas vapor concentration in scaled value (0-255)

#define BAC_THRESH 		0.10f	//threshold for maximum blood alcohol content

flash unsigned char keytbl[12]={0xed, 0xeb, 0xe7, 0xdd, 0xdb, 0xd7, 0xbd, 0xbb, 0xb7, 0x7d, 0x7b, 0x77};

unsigned char key, butnum, maybe;

unsigned int time,presTime,extra;

unsigned char keycode[5];

unsigned char keycodept;

unsigned int keyv;

unsigned int codetbl[MAXCODES];

unsigned char codenum = 0;

unsigned char locked = 0;

unsigned char pressure, codewait, addmode, delmode, adcodechange, debug;

unsigned int admincode;

unsigned char adminmode, PVflag;

unsigned char bac;

unsigned char print[8];

void initialize(void); 		//all the usual mcu stuff

void codeEntered(void); 	//code has been entered, check to see if correct

void keyPressed(void);  	//key has been pressed, store it

void getKey(void);      	//get key pressed and debounce

void adminCommand(void);	//get administrator command

void checkPressure(void);	//check to see if balloon has filled

void outputBAC(void);		//output BAC result and unlock door

interrupt [TIM0_COMP] void timer0_overflow(void)

begin

time++;

if (time>=62)

begin

time=0;

if (extra>0) extra--;

if (presTime>0) presTime--;

end

end

void main(void)

begin

initialize();           //initialize hardware components

admincode = 1234;       //initialize admincode to 1234

PVflag = 0; 		//Used to switch between vapor and pressure sensor

keycodept = 0;          //Used to track the number of keys in a punched-in code

adminmode = 0;          // Whether or not user is in administration mode

codewait = 0;           // If the code is waiting for user input (admin mode)

lcd_clear();

addmode = 0;            // mode to add codes (admin mode)

delmode = 0;            // mode to delete codes

debug =0;               // debug mod for program testing

adcodechange = 0;       // mode to change administration code

while(1)

begin

//pressure = 0;

if (debug==0)

begin

getKey();                 // check if key was pressed

if (butnum!=0) keyPressed();         // if key was pressed, store it

if (keycodept==CODELENGTH) codeEntered();     //if full code entered, check it versus known codes

else if (adminmode==1 && keycodept==1) adminCommand();    // if in administration mode, perform action

if (locked==0)

begin

if (PVflag == 0) checkPressure();             // first check pressure

else if (PVflag == 1) outputBAC();            // if flag is tripped, check BAC

end

end

else                // debug mode

begin

while(1)

begin

//checkPressure();

outputBAC();

delay_ms(200);

end

end

end

end

void codeEntered(void)

begin

int i;

keycodept=0;

keyv=0;

keycode[CODELENGTH] = '\0';

keyv = atoi(keycode);

for(i=0;i<5;i++) keycode[i] = 0;

// if adding, removing, or changing codes, set flags

if (addmode==1 || delmode==1 || adcodechange==1)

begin

codewait = 0;

adminmode = 1;

keycodept = 1;

end

else

begin

//first check to see if code matches administration code

if(admincode==keyv)

begin

adminmode = 1;

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Admin: ");

return;

end

// if door is not in permanent lock mode, check valid pass codes

if (locked==0)

begin

for(codenum=0;codenum<MAXCODES;codenum++)

if (codetbl[codenum]==keyv) break;

if (codenum==MAXCODES || keyv==0)

begin

//extra=t1;

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Bad Code");

//while(extra>0);

delay_ms(t1);

lcd_clear();

end

else

begin

//extra=t1;

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Unlocked");

PORTD.4 = 1;

//while(extra>0);

delay_ms(t1);

PORTD.4 = 0;

lcd_clear();

end

end

else

begin

//extra=t1;

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Locked");

//while(extra>0);

delay_ms(t1);

lcd_clear();

end

end

end

void keyPressed(void)

begin

keycode[keycodept++]=butnum+0x30;                      // converts button to standard ASCII format

if (keycode[keycodept-1]==0x3B) keycode[keycodept-1] = 0x30;	//corrects for zero button

butnum=0;

lcd_clear();

if(adminmode==0)

begin

lcd_gotoxy(0,0);

lcd_puts(keycode);

end

end

void getKey(void)

begin

//Gets the Low 4 bits of key

DDRB = 0x0f;

PORTB = 0xf0;

delay_us(5);

key = PINB;

//Grabs the high 4 bits of key

DDRB = 0xf0;

PORTB = 0x0f;

delay_us(5);

key = (key | PINB);

if (key!=0xff)//something is pressed

begin

for(butnum=0; butnum<MAXKEYS; butnum++)

if(keytbl[butnum]==key)  break;

if (butnum==MAXKEYS) butnum=0; // if no matching number was found, invalid button press

else

begin

butnum++;	   //adjust by one to make range 1-16

maybe = key;       //stores key for debounce

extra = t3;

delay_ms(30);

//Gets the Low 4 bits of key

DDRB = 0x0f;

PORTB = 0xf0;

delay_us(5);

key = PINB;

//Grabs the high 4 bits of key

DDRB = 0xf0;

PORTB = 0x0f;

delay_us(5);

key = (key | PINB);    //save number

if (key!=maybe) butnum=0;//it was a false reading

else

begin

while(key==maybe) //key is still pressed

begin

//Gets the Low 4 bits of key

DDRB = 0x0f;

PORTB = 0xf0;

delay_us(5);

key = PINB;

//Grabs the high 4 bits of key

DDRB = 0xf0;

PORTB = 0x0f;

delay_us(5);

key = (key | PINB);    //save number

end

end

end

end

else butnum=0; //no button is pressed

end

void checkPressure(void)

begin

ADCSR.6=1;                   // start another conversion

pressure = ADCH;             // read pressure from ADC

if (pressure < PRESSURE_THRESH)    // if pressure is less than threshold, cavity is being filled

begin

// delete any partial codes that may have been punched in

keycodept=0;

keyv=0;

// pause for 10 seconds for vapor to settle

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Reading...");

ADMUX=0b00100000;

extra=30000;

while(extra>0)

begin

ADCSR.6 = 1;

pressure = ADCH;

lcd_gotoxy(13,0);

sprintf(print,"%d",pressure);

//lcd_puts(print);

extra--;

end

PVflag = 1;           // trip flag to invoke gas sensor

ADMUX=0b00100001;     // switch to gas sensor's ADC channel

end

end

void outputBAC(void)

begin

extra=20000;

while(extra>0)         // measure BAC until it has settled

begin

ADCSR.6=1;

bac = ADCH;

extra--;

end

if (debug==0)

begin

if(bac<VAPOR_THRESH)        // if user is sober, unlock door

begin

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Unlocked");

lcd_gotoxy(13,0);

sprintf(print,"%d",bac);

lcd_puts(print);

PORTD = 0xff;       // activate solenoid

delay_ms(t2);

lcd_clear();

PORTD = 0x00;	    // deactivate solenoid

end

else                        // if user is not sober, keep door locked

begin

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("INTOXICATED!");

lcd_gotoxy(13,0);

sprintf(print,"%d",bac);

lcd_puts(print);

delay_ms(t1);

lcd_clear();

end

PVflag=0;                   // set flags for next pressure reading

ADMUX=0b00100000;

end

else

begin

ADMUX=0b00100001;

ADCSR.6 = 1;

bac = ADCH;

lcd_clear();

lcd_gotoxy(0,0);

sprintf(print,"%d",bac);

lcd_puts(print);

end

end

void adminCommand(void)

begin

//administration functions (lock, unlock, add code, rem code, change admin code, etc.)

keycodept = 0;

keycode[0] = keycode[0] - 0x30;

if (keycode[0]==0)	// exit administration mode

begin

lcd_clear();

adminmode = 0;

end

if (keycode[0]==1)	//lock the door, no further breathalyzer readings

begin

locked=1;

extra=t1;

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Locked");

//while(extra>0);

delay_ms(t1);

lcd_clear();

adminmode = 0;

end

if (keycode[0]==2)	//unlock the door

begin

locked=0;

extra=t1;

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Normal Mode");

//while(extra>0);

delay_ms(t1);

lcd_clear();

adminmode=0;

end

if (codewait==0 && addmode==1)          //if code to be added is complete

begin

for(codenum=0;codenum<MAXCODES;codenum++) if (codetbl[codenum]==0) break;

codetbl[codenum]=keyv;

adminmode = 0;

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Code Added");

delay_ms(t1);

lcd_clear();

addmode = 0;

codewait = 0;

end

if (keycode[0]==3)            // add user keycode: start point

begin

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Add Code");

delay_ms(t1);

lcd_clear();

codewait = 1;

addmode = 1;

adminmode = 0;

end

if (codewait==0 && delmode==1)       // if code to be deleted is complete

begin

for(codenum=0;codenum<MAXCODES;codenum++) if (codetbl[codenum]==keyv) break;

codetbl[codenum]=0;

adminmode = 0;

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Code Deleted");

delay_ms(t1);

lcd_clear();

delmode = 0;

codewait = 0;

end

if (keycode[0]==4)                  // delete user keycode: start point

begin

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Delete Code");

delay_ms(t1);

lcd_clear();

codewait = 1;     //add code

delmode = 1;

adminmode = 0;

end

if (keycode[0]==5)                // debug mode

begin

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Debug");

delay_ms(t1);

lcd_clear();

debug=1;

end

if (codewait==0 && adcodechange==1)        // if admin code to be changed is complete

begin

admincode = keyv;

adminmode = 0;

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Admin Changed");

delay_ms(t1);

lcd_clear();

adcodechange = 0;

codewait = 0;

end

if (keycode[0]==9)                // Change from the default administration code: start point

begin

lcd_clear();

lcd_gotoxy(0,0);

lcd_putsf("Change Code");

delay_ms(t1);

lcd_clear();

codewait = 1;     //add code

adcodechange = 1;

adminmode = 0;

end

end

void initialize(void)

begin

DDRA = 0x00;           // set PORTA to inputs for gas and pressure sensors

DDRD = 0xFF;       	// set PORTD to output for solenoid, D.0 is solenoid output

PORTD = 0x00;          // initialize to off

lcd_clear();

lcd_gotoxy(0,0);

//set up timer 0

OCR0=249;	   			//1 mSec

TIMSK=2;	   			//turn on timer 0 cmp-match ISR

TCCR0=0b00001011;		//prescalar to 64  and Clr-on-match

//init the task timers

time=0;

extra=0;

//init the A to D converter

//channel zero/ left adj /EXTERNAL Aref

//!!!CONNECT Aref jumper!!!!

ADMUX = 0b00100000;

//enable ADC and set prescaler to 1/128*16MHz=125,000

//and clear interupt enable

//and start a conversion

ADCSR = 0b11000111;

//A.0 is pressure sensor

//A.1 is vapor sensor

//crank up the ISRs

#asm

sei

#endasm

lcd_init(LCDwidth);      	//initialize the display

lcd_clear();

end