#include <Mega32.h>

#include <stdio.h>

#include <math.h>

#include <delay.h>

#define begin {

#define end   }

#define dTime 1000

#define srTime 300

#define slTime 200

#define rTime 100

#define left 0

#define right 1

#define forward 2

#define stop 3

char mic1, roundFinished, firstFinished, secondFinished;										//mic ADC

char m1value, m2value, m3value;																							//mic signals

int driveTime, steerTime, resetTime;																				//timers for driving

char drive, steer, enableResetTime, direction, turnedLeft, turnedRight;			//driving var

void initialize(void);

void resetWheel(void);

//==================================

//Timer0 Interrupt

interrupt [TIM0_COMP] void tim0isr(void)

begin

//rear motor timer

if (drive==1 && driveTime>0) driveTime--;

//steering motor timer

if (steer==1 && steerTime>0) steerTime--;

//reseting steering wheel timer

if (enableResetTime==1) resetTime--;

end //timer0 ISR

//==================================

//ADC Interrupt

interrupt [ADC_INT] void adcComp(void)

begin

if (mic1==1)								//first mic ADC

begin

m1value = ADCH;					//retrieve ADC value

ADMUX = 0b01100010;			//switch pin

mic1 = 2;

firstFinished = 1;

end

else

begin

if (mic1==2)							//second mic ADC

begin

m2value = ADCH;					//retrieve ADC value

ADMUX = 0b01100011;			//switch pin

mic1 = 3;

secondFinished = 1;

end

else											//third mic ADC

begin

m3value = ADCH;					//retrieve ADC value

ADMUX = 0b01100001;			//switch pin

mic1 = 1;

roundFinished = 1;

end

end

end //ADC ISR

//==================================

//initialize

void initialize(void)

begin

DDRA = 0x00;				//ADC

DDRB = 0xff;				//motor B7=f/r B6=l/r B5=pwm

DDRC = 0xff;				//LED

DDRD = 0xff;				//LED

//TIM0 SETUP Interrupt every 1ms

OCR0 = 249;

TIMSK = 0b00000010;

TCCR0 = 0b00001011;

//ADC SETUP

//init the A to D converter

//channel zero/ left adj /EXTERNAL Aref

ADMUX = 0b01100001;

//enable ADC and set prescaler to 1/128*16MHz=125,000

ADCSR = 0b10001110;

//init variables

mic1 = 1;

firstFinished = 0;

secondFinished = 0;

roundFinished = 0;

drive = 0;

steer = 0;

driveTime = dTime;

steerTime = srTime;

resetTime = rTime;

turnedRight = 0;

turnedLeft = 0;

#asm

sei

#endasm

end //initialize

//==================================

//resetWheel

void resetWheel(void)

begin

if (turnedLeft==1)			//previous turned left, turn right

begin

PORTB.6 = 1;

PORTB.5 = 1;

end

if (turnedRight==1)			//previous turned right, turn left

begin

PORTB.6 = 0;

PORTB.5 = 1;

end

turnedLeft = 0;

turnedRight = 0;

enableResetTime = 1;

resetTime = rTime;

end

//==================================

//main

void main(void)

begin

initialize();

PORTD=0xff;				//turn LED off

delay_ms(2000);

ADCSR.6 = 1;			//start ADC

while(1)

begin

if (resetTime==0 && enableResetTime==1)				//reseting wheels done

begin

PORTB.5 = 0;																//stop PWM

enableResetTime = 0;

delay_ms(2000);															//delay for noise from the motor

ADCSR.6 = 1;																// anoter ADC

end

if (driveTime==0 && drive==1)						//forward drive done

begin

drive = 0;

direction = stop;

PORTB.7 = 0;

if (turnedLeft==1 || turnedRight==1)

begin

resetWheel();

PORTC=0b00110011;

end

else

begin

delay_ms(2000);

ADCSR.6 = 1;

end

end

if (steerTime==0 && steer==1)						//steering done

begin

PORTC = 0xaa;

steer = 0;

direction = stop;

PORTB.5 = 0;

end

if (firstFinished==1)													//first mic ADC done

begin

firstFinished = 0;

ADCSR.6 = 1;

end

if (secondFinished==1)												//second mic ADC done

begin

secondFinished = 0;

ADCSR.6 = 1;

end

if (roundFinished==1)													//third mic ADC done

begin

roundFinished = 0;

//right turn

if (m1value>=180 && m2value<180 &&m3value<180)	//first mic closest to the source

begin

roundFinished = 0;

direction = right;

end

//left turn

if (m1value<180 && m2value>=180 && m3value<180)	//second mic closest to the source

begin

roundFinished = 0;

direction = left;

end

//forward

if (m1value<180 && m2value<180 && m3value>=180)	//third mic closest to the source

begin

direction = forward;

roundFinished = 0;

end

if (m1value<180 && m2value<180 && m3value<180)	//no signals received

begin

roundFinished = 0;

ADCSR.6 = 1;

end

if (m1value>=180 && m2value>=180 && m3value>=180)	//reset

begin

PORTD=0x00;

initialize();

roundFinished = 0;

end

//driving right b6=0 left b6=1

if (direction==forward)				//drive forward

begin

PORTC = 0b01111111;

drive = 1;

steer = 0;

direction = stop;

driveTime = dTime;

PORTB.7 = 1;

end

if (direction==left)					//drive left

begin

PORTC = 0b10111111;

drive = 1;

steer = 1;

direction = stop;

driveTime = dTime;

steerTime = slTime;

PORTB.7 = 1;

PORTB.6	=	0;

PORTB.5	=	1;

turnedLeft = 1;

end

if (direction==right)					//drive right

begin

PORTC = 0b11011111;

drive = 1;

steer = 1;

direction = stop;

driveTime = dTime;

steerTime = srTime;

PORTB.7 = 1;

PORTB.6	=	1;

PORTB.5	=	1;

turnedRight = 1;

end

end

end //while

end //main