## Slide 1: Project: Modeling a Microvascular Network on a Chip
Idea: To characterize a simple model of the microvascular system using a microfluidic device
Potential Uses:
  Simulate clot, stroke, plaque buildup in arteries
  Discern effect of vessel blockage or occlusion on blood pressure
Components:
  PDMS microdevice
  Tubing
  Syringe pump
  Silicone sealant
  Beads for visualization
  Microscope
  Image capture software
  Image analysis software

## Slide 2: Overview
  Measure flow velocities within model network before and after a blockage (mimicking an occlusion of a blood vessel or clot like during a stroke) and track the redistribution of flow when a channel is occluded.
  Lab will be followed by a session where you will theoretically calculate the pressure and velocity in each channel before and after blockage using MATLAB. You will then compare your calculated pressure and velocities with your measured velocities.

## Slide 3: What is Microfluidics: What’s in a name?
Infer: manipulation of minute quantities of fluids (L and G) …
  inside devices made using advanced microfab tools (CNF).
  Applies ultra-precise fab technology to conventionally “messy” fields like biology (dishes, plates) and chemistry (vats, reaction vessels)
  New field – emerged early 90s: Andreas Manz, George Whitesides
  Why?
    Unique physics at microscale permits novel creations:
      Laminar flow
      High SA/V ratio – surface tension (droplet) >> gravity (sedimentation)
    Reduces amounts of reagents needed
    Permits more orderly, systematic approach to bio-related problems, reduces physical effort: drug discovery, cytotoxicity assays, protein crystallization (for x-ray crystallography)
    Disposable, parallel operation, increased reliability
  Applications:
    Biomimesis, diagnostic devices, biosensors, cell sorting, enrichment, storing

## Slide 4: Examples of Microfluidics
LSI
Body on chip
Concentration gradient
Sperm sorter for IVF
Portable medical diagnostics
Traction force microscopy

## Slide 5: Your Microfluidic Device
Mimics this

## Slide 6: Procedure: Before Clot
PDMS devices made for you
Fill syringe with bead (10um dia.) solution
Connect needle to syringe
Connect tubing to needle
Place syringe in syringe pump
Flow @ 50uL/min to flush out bubbles
Reduce flow rate to 1-5uL/min
Capture series of images to track beads in each channel of device
  V = d/t

## Slide 7: Procedure: Clot
Disconnect device from pump
Using empty syringe, introduce air to dry device
Punch hole in desired channel with punch
Remove plug of PDMS
Inject sealant to block channel
Cure @ 60C for 10min
Repeat process: track beads in each channel

## Slide 8: How Many Channels?
1
2
3
4
5
6
7
8
9

## Slide 9: Results and Data Analysis Expected
Average velocity for each channel before blockage
Average velocity for each channel after blockage
Prediction of flow pattern after channel blockage
Bead Motion Analysis:
  Want to track at least 10 beads in each channel
  Track beads in each channel over several frames
  Not interested in instantaneous velocity of beads (changes from frame to frame)
  Interested in average velocity (total distance traveled / time observed)
  Bin data to generate histogram (data partitioned into intervals and frequency of occurrence plotted)

## Slide 10: Note on Bead Motion
In pressure-driven flow, velocity profile of fluid is parabolic:
Velocity is maximum in center of channel
Velocity is minimum near walls of channel

## Slide 11: Analysis: Circuit Analog
In analyzing a microfluidic device, it is useful to make an analogy to an electrical circuit:
Pressure → Voltage
Flow Rate → Current
Hydraulic Resistance → Electrical Resistance
Volumetric flow rate = average linear velocity * cross-sectional area of channel
Ohm’s Law:
  V = IR
  Pressure = Volumetric Flow Rate * Channel Resistance
Ground = reference potential → same pressure
KCL:
  Conservation of charge → conservation of mass:
    Flow rate into a node MUST equal flow rate out of that node
    Nothing collects at node
i1 →
←i2
i3 ↓
Convention: Define flow into node as + and flow out of node as –
I1 + i2 – i3 = 0
13 = i1+i2

## Slide 12: Circuit Analysis
Resistances are either in series or parallel
RT = R1+R2+R3 = 1000+2000+3000 = 6000 ohm
Sum is ALWAYS greater than any single resistance
RT = 1 / (1/R1 + 1/R2 + 1/R3) = 1/ (1/1000 + 1/2000 + 1/3000) = 545 ohm
Sum is ALWAYS less than any single resistance
Special Case: 2 in parallel:
RT = R1*R2 / (R1+R2)
Series:
Parallel:

## Slide 13: Example: Resistance Network

## Slide 14
1. R1 and R2 in series = 6k

## Slide 15
2. R3 and R4 in series = 500 ohm

## Slide 16
3. 500 ohm in parallel with 1500 ohm = 375 ohm

## Slide 17
Remaining resistors in series = 6000 + 375 + 250 + 400 = 7025 ohm

## Slide 18: Pressure Drop Along Channel Equation valid only if w >>h

## Slide 19: Fabrication: How Are Microfluidic Devices Made?
Pattern is defined on surface (2D) and then transferred into vertical plane
Process flow – depicted as a cross-sectional view, each step showing execution of one step (addition of layer, exposure, removal of layer, etc.)

## Slide 20: Process Flow: Soft-Lithography
1) Spin SU-8
Si
SU-8
Mask
2) Expose
3) Develop
4) Apply Anti-stick monolayer
6) Plasma treat + bond
glass
2) Expose
mask
5) Cast PDMS

## Slide 21: END