## Slide 1: MATLAB Session for CURIE
Summer 2011

## Slide 2: You Will do This for Unblocked and Blocked Devices
Need to find inlet pressure to input into MATLAB program

## Slide 3: First: Find RT
μ = Viscosity = 0.89cp =0.0089g/cm-s = 0.00000089g/um-s =
0.00000089 kg/mm-s
MATLAB program wants these units

## Slide 4: Find RT by Finding Effective Resistance of Network
Find Total Resistance by first finding resistance of each channel
THEN simplifying circuit to one equivalent resistor
THEN, using Ohm’s Law, find ∆P
THEN, from ∆P, Find Pin
∆P = Pin - Pout

## Slide 5: Individual Resistances: Watch Units!
Channel Number | Width (um) | Height (um) | Length(um) | Resistance
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
MATLAB wants pressures in units of Pascals:
1 Pa = 1 kg/m-s^2 = 1 kg/mm-s^2

## Slide 6
D,E,F in series so R = RD+RE+RF
B in parallel with B
(B in parallel with B), in series with C
Unblocked

## Slide 7: Circuit Simplification
We see that 3 resistances are in parallel: brown, blue, and brown:
Rcombo = 1/ [(1/brown)+(1/blue)+(1/brown)]
Then we see we have four resistances in series: red, green, Rcombo, and red
RT = .96 kg/mm^4-s

## Slide 8: Find ∆P
V=IR
∆P = QRT
Q = 2uL/min (or what you set it to in lab)
Q = (2uL/min)*(mm3/uL)*(1min/60s) = 0.0333 mm3/s
∆P = (.0333 mm3/s)*(.96 kg/mm4-s) = 0.031968kg/mm-s2
(0.031968kg/mm-s2)*(1000mm/1m) = 31.97kg/(m-s2)
31.97kg/(m-s2)*(1 N/(kg-m/s2)) = 31.97N/m2 = 31.97Pa
∆P = 31.97 Pa

## Slide 9: Find Pin
∆P = Pin – Pout
Pin = ∆P + Pout
Pout is =?
Outlet tubing connected to atmosphere so…

## Slide 10: Pressure cont.
Pout = Patm = 14.7 psi = 760 mmHg = 101325 Pa
Pin = 101325 + = 31.97 Pa = 101 356.97 Pa

## Slide 11: MATLAB: Label Nodes
N1
N2
N3
N4
N6
N8
N9
N7
N5
Number of elements? 11

## Slide 12: MATLAB cont.
Modify example “data.txt” with this network (different nodes, channel widths, channel lengths)
Run program

## Slide 13: Check:
V=IR
∆P = QRT
RT = ∆P / Q
Should be same as what you obtained through circuit simplification!

## Slide 14: Blocked Channel
Blocked channel corresponds to open circuit (that element removed from circuit)

## Slide 15: With open circuit element removed:
D,E,F in series so R1 = RD+RE+RF
B,F,E,D in series so R2 = RB+RD+RE+RF
C in parallel with R2

## Slide 16: Need to simplify your blocked device…
Same procedure as for unblocked device
Is the resistance higher or lower or same?

## Slide 17: Questions?
What does this lab tell you about the blood pressure inside someone with constricted or blocked blood vessels?
Is the analogy perfect?